Derivation of Equations Used in bfield_server.cpp
# Introduction
Based FDTD update equations on a lecture series by Raymond C. Rumpf at CEM, UTEP, http://emlab.utep.edu/ee5390cem.htm, and Understanding the Finite-Difference Time-Domain Method, 2018, John Schneider, 2018. The source injection method comes from Introduction to the Finite-Difference Time-Domain (FDTD) Method for Electromagnetics, 2011, Stephen D. Gedney.

Using Rumpf's conventions:
— E on whole time step, H on half (see 15.7).
— Normalized H (H~ = H/Z0), in V/m.

Equation numbers from CEM refer to (Lecture.Slide). Those from Schneider have a 'U' prepended, and from Gedney, a 'G'.
# gaussian()
Taken from the Gaussian function Wiki page.
f(x) = a e^-{ (x-b)^2 / (2 c^2)}
where a is the height, b is the center position, and c is the RMS width.

LC’s hard gaussian pulse source appears to be:
f(t) = s e^{-4(ln 2){(t-{t_R %sigma_R / %pi})^2 / t_R^2}}
LC appears to have t_R = FWTM (Full Width at Tenth Maximum), which is 2 sqrt( 2 ln 2 ) c .
# MatBlock::place()
Material Block Placement. For placement of blocks on any boundary (and for proper placement in the 1/2-cell-displaced E field), consider on each axis the overlapping area between a function that is 1 from matStart.x to matEnd.x, and another function that is a triangle of height 2 and base 1, centered on the position in question:
f_mat(x) = left lbrace matrix { 1 # alignl for~ x_s <= x < x_e ## 0 # alignl otherwise } right none	(3.1)
f_pos(x) = left lbrace matrix { 4(x+1over2-x_p) # alignl for~ -1over2 <= (x-x_p) < 0 ## -4(x-1over2-x_p) # alignl for~ 0 <= (x-x_p) < 1over2 ## 0 # alignl otherwise } right none	(3.2)

Integrating just (3.1):
c ~=~ left none x right rline_{x_e}^{x_s} ~=~ x_s - x_e ✔	(3.3)
Integrating just (3.2):
c ~=~ left none (2x^2+(2-4x_p)x) right rline_{x_p-1over2}^{x_p} ~+~ left none (-2x^2+(-2+4x_p)x) right rline_{x_p}^{x_p+1over2}
c ~=~ {(2x_p^2+(2-4x_p)x_p) ~-~ (2(x_p-1over2)^2+(2-4x_p)(x_p-1over2))} newline +~ (-2(x_p+1over2)^2+(-2+4x_p)(x_p+1over2)) ~-~ (-2x_p^2+(-2+4x_p)x_p)
c ~=~ (2x_p^2+2x_p-4x_p^2-2x_p^2+2x_p-1over2-2x_p+4x_p^2+1-2x_p) newline +~ (-2x_p^2-2x_p-1over2-2x_p+4x_p^2-1+2x_p+2x_p^2+2x_p-4x_p^2)
c ~=~ ((0)x_p^2 + (0)x_p +1over2) ~+~ ((0)x_p^2 + (0)x_p +1over2) ~=~ 1 ✔	(3.4)

The combined function is:
f(x) = left lbrace matrix { 4(x+1over2-x_s) # alignl for~ -1over2 <= (x-x_s) < 0 ## -4(x-1over2-x_e) # alignl for~ 0 <= (x-x_e) < 1over2 ## 0 # alignl otherwise } right none
Then we want to integrate this function:
c = int from x_p-1over2 to x_p+1over2 f(x) dx
# Source::injectAll()
-----------------
180331:

Source injecting current into E field:
color silver {nospace{%iDELTA E_z} ~=~ -nospace{%iDELTA t} over %ivarepsilon left [ I_z over {nospace{%iDELTA x} nospace{%iDELTA y}} right ]}
For example: dE = -(4.16945e-13 s) / (8.8542e-12 F/m) * ((0.15V / 50 ohms) / (0.25mm * 0.25mm)) = -2260 V/m ???

From Gedney:

color purple {E_{z,i,j,k+1/2}^{n+1/2} ~=~ { { {%ivarepsilon over nospace{%iDELTA t}} ~-~ nospace{%iDELTA z} over {nospace{%iDELTA x} nospace{%iDELTA y}2R_TH} } over { {%ivarepsilon over nospace{%iDELTA t}} ~+~ nospace{%iDELTA z} over {nospace{%iDELTA x} nospace{%iDELTA y}2R_TH} } } E_{z,i,j,k+1/2}^{n-1/2} ~+~ { 1 over { %ivarepsilon over nospace{%iDELTA t} ~+~ nospace{%iDELTA z} over {nospace{%iDELTA x} nospace{%iDELTA y}2R_TH} } } } newline color purple { left [ left ( {H_{y,i+1/2,j,k+1/2}^n - H_{y,i-1/2,j,k+1/2}^n} over nospace{%iDELTA x} right ) ~-~ left ( {H_{x,i,j+1/2,k+1/2}^n - H_{x,i,j-1/2,k+1/2}^n} over nospace{%iDELTA y} right ) ~-~ {V_{oc,i,j,k+1/2}^n} over {nospace{%iDELTA x} nospace{%iDELTA y} R_TH} right ] }	(G4.28)
Converting this to E-on-the-whole-time-step and normalized H conventions:
H = {tilde H} / { %ieta_0 }	(4.1)
 E_{z,i,j,k+1/2}^n ~=~ { { {%ivarepsilon over nospace{%iDELTA t}} ~-~ nospace{%iDELTA z} over {nospace{%iDELTA x} nospace{%iDELTA y}2R_TH} } over { {%ivarepsilon over nospace{%iDELTA t}} ~+~ nospace{%iDELTA z} over {nospace{%iDELTA x} nospace{%iDELTA y}2R_TH} } } E_{z,i,j,k+1/2}^{n-1} ~+~ { 1 over { %ieta_0 left ( %ivarepsilon over nospace{%iDELTA t} ~+~ nospace{%iDELTA z} over {nospace{%iDELTA x} nospace{%iDELTA y}2R_TH} right ) } } newline left [ left ( {{tilde H}_{y,i+1/2,j,k+1/2}^{n-1/2} - {tilde H}_{y,i-1/2,j,k+1/2}^{n-1/2}} over nospace{%iDELTA x} right ) ~-~ left ( {{tilde H}_{x,i,j+1/2,k+1/2}^{n-1/2} - {tilde H}_{x,i,j-1/2,k+1/2}^{n-1/2}} over nospace{%iDELTA y} right ) ~-~ {%ieta_0 V_{oc,i,j,k+1/2}^{n-1/2}} over {nospace{%iDELTA x} nospace{%iDELTA y} R_TH} right ]	(4.2)
Substituting sigma and J:
 E_{z,i,j,k+1/2}^n ~=~ { { 1 - {%isigma_TH^E} } over { 1 + {%isigma_TH^E} } } E_{z,i,j,k+1/2}^{n-1} ~+~ {nospace{%iDELTA t} over {%ieta_0 %ivarepsilon (1 + {%isigma_TH^E}) } } newline left [ left ( {{tilde H}_{y,i+1/2,j,k+1/2}^{n-1/2} - {tilde H}_{y,i-1/2,j,k+1/2}^{n-1/2}} over nospace{%iDELTA x} right ) ~-~ left ( {{tilde H}_{x,i,j+1/2,k+1/2}^{n-1/2} - {tilde H}_{x,i,j-1/2,k+1/2}^{n-1/2}} over nospace{%iDELTA y} right ) ~-~ J' right ]	(4.3)
size 10.5 "where " {%isigma_TH^E = {nospace{%iDELTA t} nospace{%iDELTA z}} over {%ivarepsilon nospace{%iDELTA x} nospace{%iDELTA y} 2 R_TH}} ,~ {J' = {%ieta_0 V_{oc,i,j,k+1/2}^{n-1/2}} over {nospace{%iDELTA x} nospace{%iDELTA y} R_TH}}
size 10.5 "Forgoing non-cubic cells for now, so" nospace{%iDELTA x} = nospace{%iDELTA y} = nospace{%iDELTA z} size 10.5 " and we can remove the inner-loop divides:"
 E_{z,i,j,k+1/2}^n ~=~ m_E1 E_{z,i,j,k+1/2}^{n-1} ~+~ newline {hat m}_E2 left [ left ( {{tilde H}_{y,i+1/2,j,k+1/2}^{n-1/2} - {tilde H}_{y,i-1/2,j,k+1/2}^{n-1/2}} right ) ~-~ left ( {{tilde H}_{x,i,j+1/2,k+1/2}^{n-1/2} - {tilde H}_{x,i,j-1/2,k+1/2}^{n-1/2}} right ) ~-~ hat J right ]	(4.4)
size 10.5 "where " {%isigma_TH^E = {nospace{%iDELTA t}} over {%ivarepsilon nospace{%iDELTA x} 2 R_TH}} ,~ {hat J = {%ieta_0 V_{oc,i,j,k+1/2}^{n-1/2}} over {nospace{%iDELTA x} R_TH}} ,~ {m_E1 = {1 - {%isigma_TH^E}} over {1 + {%isigma_TH^E}}} ,~ {{hat m}_E2 = nospace{%iDELTA t} over {nospace{%iDELTA x} %ieta_0 %ivarepsilon (1 + {%isigma_TH^E})}}
size 10 "ste:" %isigma_TH^E,~~ size 10 "z0:" %ieta_0,~~ size 10 "ep0:" %ivarepsilon_0,~~ size 10 "epr:" %ivarepsilon_r,~~ size 10 "dx:" nospace{ %iDELTA x},~~ size 10 "val:" V_oc

// current density (*z0 due to mE2, ~H)
double epr = 1.;
double sige = 0.;
double sige += 1/(R*dx);
double ste = sige*dt / (ep0*epr*2);
double mE1 = (1. - ste) / (1. + ste);
double mE2 = dt / ((1. + ste) * dx*z0*ep0*epr);
double J = -z0 * val / (dx*R);
switch (src->axis) {
    case 0:
        sp->mE1.x[idx] = mE1;
        sp->mE2.x[idx] = mE2;
        sp->J.x[idx] = J / sn.i;
        break;
...
    E.z = mE1.z * E.z +
        mE2.z * ((H.y - (cp-i1)->H.y) -
        (H.x - (cp-J1)->H.x) - J.z);

## Dimensional Analysis
For (4.3):
%isigma_TH^E ~toward~ {(s) (m)} over {(kg^-1 m^-3 s^4 A^2) (m) (m) (kg^1 m^2 s^-3 A^-2)} ~toward~ 1 ✔
J' ~toward~ {(ohm) (kg^1 m^2 s^-3 A^-1)} over {(m) (m) (ohm)} ~toward~ (kg^1 m^0 s^-3 A^-1)
For (4.4):
%isigma_TH^E ~toward~ {(s)} over {(kg^-1 m^-3 s^4 A^2) (m) (kg^1 m^2 s^-3 A^-2)} ~toward~ 1 ✔
{hat J} ~toward~ {(ohm) (kg^1 m^2 s^-3 A^-1)} over {(m) (ohm) } ~toward~ (kg^1 m^1 s^-3 A^-1)
For true current density:
J = {hat J} over {%ieta_0 nospace{%iDELTA x}} ~toward~ (kg^1 m^1 s^-3 A^-1) over { (kg^1 m^2 s^-3 A^-2) (m) } ~toward~ A over { m^2 } ✔
# OuterSpace::initPMLarea()
Derivation of PML area Update Equations. Maxwell's equations for diagonal anisotropic media, incorporating loss
alignl stack{left[ alignc matrix {0 # -{partial over {partial z}} # {partial over nospace{partial y}} ## {partial over {partial z}} # 0 # -{partial over {partial x}} ## -{partial over nospace{partial y}} # {partial over {partial x}} # 0} right] left[ matrix {H_x ## H_y ## H_z} right] ~=~ j %iomega %ivarepsilon_0 left[ matrix{ %ivarepsilon_x + %isigma_x^E / {j %iomega} # 0 # 0 ## 0 # %ivarepsilon_y + %isigma_y^E / {j %iomega} # 0 ## 0 # 0 # %ivarepsilon_z + %isigma_z^E / {j %iomega} } right] left[ matrix {E_x ## E_y ## E_z} right] # left[ alignc matrix {0 # -{partial over {partial z}} # {partial over nospace{partial y}} ## {partial over {partial z}} # 0 # -{partial over {partial x}} ## -{partial over nospace{partial y}} # {partial over {partial x}} # 0} right] left[ matrix {E_x ## E_y ## E_z} right] ~=~ -j %iomega %imu_0 left[ matrix{ %imu_x + %isigma_x^H / {j %iomega} # 0 # 0 ## 0 # %imu_y + %isigma_y^H / {j %iomega} # 0 ## 0 # 0 # %imu_z + %isigma_z^H / {j %iomega} } right] left[ matrix {H_x ## H_y ## H_z} right] }	(L13.S19)

PML parameters:
alignl stack { {alignc [ s ] = [ %imu_r ] = [ %ivarepsilon_r ] = left[ matrix { a # 0 # 0 ## 0 # b # 0 ## 0 # 0 # c } right] ~~~ a = b = 1 over c} # [ s_z ] = {alignc left[ matrix { s_z # 0 # 0 ## 0 # s_z # 0 ## 0 # 0 # s_z^-1 } right] ~~~ s_z = %ialpha - j %ibeta } }	(L13.S36)

PML along all the borders:
[ s_i ] ~=~ left[ matrix { s_i^-1 # 0 # 0 ## 0 # s_i # 0 ## 0 # 0 # d_i } right]	(L13.S37a)

Combined into a single tensor quantity:
[s] ~=~ [s_x] cdot [s_y] cdot [s_z] ~=~ left[ matrix { {s_y s_z} over s_x # 0 # 0 ## 0 # {s_x s_z} over s_y # 0 ## 0 # 0 # {s_x s_y} over s_z } right]	(L13.S37b)

Maxwell's equations with uniaxial PML:
nabla times vec E = k_0 [ %imu_r ] [ s ] vec tilde H ~~~ nabla times vec tilde H = k_0 [ %ivarepsilon_r ] [ s ] vec E	(L13.S40a)

Move PML tensor to the left side:
[ s ]^-1 nabla times vec E = k_0 [ %imu_r ] vec tilde H ~~~ [ s ]^-1 nabla times vec tilde H = k_0 [ %ivarepsilon_r ] vec E	(L13.S41a)

Curl operator is now:
[s]^-1 nabla times ~=~ left[ matrix { s_z^-1 s_y^-1 s_x # 0 # 0 ## 0 # s_z^-1 s_y s_x^-1 # 0 ## 0 # 0 # s_z s_y^-1 s_x^-1 } right] left[ matrix {0 # -{partial over {partial z}} # {partial over nospace{partial y}} ## {partial over {partial z}} # 0 # -{partial over {partial x}} ## -{partial over nospace{partial y}} # {partial over {partial x}} # 0} right] newline phantom {[s]} ~=~ left[ matrix {0 # -{s_x over s_y} left( {1 over s_z} {partial over {partial z}} right) # {s_x over s_z} left( {1 over s_y} {partial over nospace{partial y}} right) ## {s_y over s_x} left( {1 over s_z} {partial over {partial z}} right) # 0 # -{s_y over s_z} left( {1 over s_x} {partial over {partial x}} right) ## -{s_z over s_x} left( {1 over s_y} {partial over nospace{partial y}} right) # {s_z over s_y} left( {1 over s_x} {partial over {partial x}} right) # 0} right]	(L13.S41b)

size 10.5 "Factors" s_x, s_y, size 10.5 "and" s_z size 10.5 "are effectively stretching the coordinates into a complex space."

Drop the non-stretching terms:
nabla _s times ~=~ left[ matrix {0 # -{1 over s_z} {partial over {partial z}} # {1 over s_y} {partial over nospace{partial y}} ## {1 over s_z} {partial over {partial z}} # 0 # -{1 over s_x} {partial over {partial x}} ## -{1 over s_y} {partial over nospace{partial y}} # {1 over s_x} {partial over {partial x}} # 0} right]	(L13.S43a)

Introduce loss in the PML through fictitious conductivity terms, σ' (sigma prime), which are zero in the central problem space, but gradually increase going outward in the PML boundaries.

PML loss terms:
s_i(i) ~=~ 1+{ {%isigma'_i(i)} over {j%iomega %ivarepsilon_0} } ~~~ %isigma'_i(i) = %ivarepsilon_0 over {2 %iDELTA t} left( i over L_i right)^3 newline size 10.5 {"where " i = x,y,z ", and " L_i = "length of the PML in the i direction."}	(L13.S46)

To add PML to Maxwell's equations, we do it in the frequency domain:
alignl nabla times vec E(%iomega) ~=~ -j %iomega %imu_0 [%imu_r] color blue {[s]} vec H(%iomega) newline nabla times vec H(%iomega) ~=~ %isigma vec E(%iomega) + j %iomega color blue {[s]} vec D(%iomega) ~~~ vec D(%iomega) ~=~ %ivarepsilon_0 [ %ivarepsilon_r ] vec E(%iomega)	(L13.S54)

Normalize the E field quantities according to:
vec tilde E = sqrt { %ivarepsilon_0 over %imu_0 } vec E = 1 over %ieta_0 vec E ~~~ vec tilde D = 1 over sqrt { %imu_0 %ivarepsilon_0 } vec E = c_0 vec E	(L13.S55a)

Maxwell's equations with the PML and normalized fields are:
alignl nabla times vec tilde E(%iomega) ~=~ {alignc -j %iomega [%imu_r] over c_0 [s] vec H(%iomega) } newline nabla times vec H(%iomega) ~=~ %ieta_0 %isigma vec tilde E(%iomega) + {j %iomega} over c_0 [s] vec tilde D(%iomega) ~~~ vec tilde D(%iomega) ~=~ [ %ivarepsilon_r ] vec tilde E(%iomega)	(L13.S55b)
In matrix form, and with diagonal tensors substituted:	stack { alignl left[ alignc matrix {0 # -{partial over {partial z}} # {partial over {partial y}} ## {partial over {partial z}} # 0 # -{partial over {partial x}} ## -{partial over {partial y}} # {partial over {partial x}} # 0} right] left[ matrix {tilde E_x(%iomega) ## tilde E_y(%iomega) ## tilde E_z(%iomega) } right] = {alignc -{{j %iomega} over c_0} left[ matrix { %imu_xx # 0 # 0 ## 0 # %imu_yy # 0 ## 0 # 0 # %imu_zz } right] color red {left[ matrix { s_x^-1 s_y s_z # 0 # 0 ## 0 # s_x s_y^-1 s_z # 0 ## 0 # 0 # s_x s_y s_z^-1 } right] } left[ matrix {H_x(%iomega) ## H_y(%iomega) ## H_z(%iomega) } right] } # left[ matrix {0 # -{partial over {partial z}} # {partial over {partial y}} ## {partial over {partial z}} # 0 # -{partial over {partial x}} ## -{partial over {partial y}} # {partial over {partial x}} # 0} right] left[ matrix {H_x(%iomega) ## H_y(%iomega) ## H_z(%iomega) } right] = %ieta_0 left[ matrix { %isigma_xx # 0 # 0 ## 0 # %isigma_yy # 0 ## 0 # 0 # %isigma_zz } right] left[ matrix {tilde E_x(%iomega) ## tilde E_y(%iomega) ## tilde E_z(%iomega) } right] + {j %iomega} over c_0 left[ matrix { s_x^-1 s_y s_z # 0 # 0 ## 0 # s_x s_y^-1 s_z # 0 ## 0 # 0 # s_x s_y s_z^-1 } right] left[ matrix {tilde D_x(%iomega) ## tilde D_y(%iomega) ## tilde D_z(%iomega) } right] # alignl left[ alignc matrix {tilde D_x(%iomega) ## tilde D_y(%iomega) ## tilde D_z(%iomega) } right] = left[ alignc matrix { %ivarepsilon_xx # 0 # 0 ## 0 # %ivarepsilon_yy # 0 ## 0 # 0 # %ivarepsilon_zz } right] left[ matrix {tilde E_x(%iomega) ## tilde E_y(%iomega) ## tilde E_z(%iomega) } right] }	(13.57)

Vector expansion:
nabla times vec tilde E(%iomega) = {-j %iomega [%imu_r] over c_0 [s] vec H(%iomega) } ~~toward~~ matrix { {partial tilde E_z(%iomega)} over {partial y} - {partial tilde E_y(%iomega)} over {partial z} = -j %iomega { %imu_xx over c_0}{{s_y s_z} over s_x} H_x(%iomega) ## {partial tilde E_x(%iomega)} over {partial z} - {partial tilde E_z(%iomega)} over {partial x} = -j %iomega { %imu_yy over c_0}{{s_x s_z} over s_y} H_y(%iomega) ## {partial tilde E_y(%iomega)} over {partial x} - {partial tilde E_x(%iomega)} over {partial y} = -j %iomega { %imu_zz over c_0}{{s_x s_y} over s_z} H_z(%iomega) } newline newline nabla times vec H(%iomega) = %ieta_0 %isigma vec tilde E(%iomega) + {j %iomega} over c_0 [s] vec tilde D(%iomega) ~~toward~~ matrix { {partial H_z(%iomega)} over {partial y} - {partial H_y(%iomega)} over {partial z} = %ieta_0 %isigma_xx tilde E_x(%iomega) + { {j %iomega} over c_0}{{s_y s_z} over s_x} tilde D_x(%iomega) ## {partial H_x(%iomega)} over {partial z} - {partial H_z(%iomega)} over {partial x} = %ieta_0 %isigma_yy tilde E_y(%iomega) + { {j %iomega} over c_0}{{s_x s_z} over s_y} tilde D_y(%iomega) ## {partial H_y(%iomega)} over {partial x} - {partial H_x(%iomega)} over {partial y} = %ieta_0 %isigma_zz tilde E_z(%iomega) + { {j %iomega} over c_0}{{s_x s_y} over s_z} tilde D_z(%iomega) } newline newline vec tilde D(%iomega) = [ %ivarepsilon_r ] vec tilde E(%iomega) ~~toward~~ matrix { tilde D_x(%iomega) = %ivarepsilon_xx tilde E_x(%iomega) ## tilde D_y(%iomega) = %ivarepsilon_yy tilde E_y(%iomega) ## tilde D_z(%iomega) = %ivarepsilon_zz tilde E_z(%iomega) }	(L13.S58)

Substitute si from (13.46) to get final form of Maxwell's Equations with UPML:
j %iomega left( 1 + {{%isigma'_x} over {j %iomega %ivarepsilon_0}} right)^-1 left( 1 + {{%isigma'_y} over {j %iomega %ivarepsilon_0}} right) left( 1 + {{%isigma'_z} over {j %iomega %ivarepsilon_0}} right) H_x(%iomega) = -{ c_0 over %imu_xx } left[ {partial tilde E_z(%iomega)} over {partial y} - {partial tilde E_y(%iomega)} over {partial z} right] newline j %iomega left( 1 + {{%isigma'_x} over {j %iomega %ivarepsilon_0}} right) left( 1 + {{%isigma'_y} over {j %iomega %ivarepsilon_0}} right)^-1 left( 1 + {{%isigma'_z} over {j %iomega %ivarepsilon_0}} right) H_y(%iomega) = -{ c_0 over %imu_yy } left[ {partial tilde E_x(%iomega)} over {partial z} - {partial tilde E_z(%iomega)} over {partial x} right] newline j %iomega left( 1 + {{%isigma'_x} over {j %iomega %ivarepsilon_0}} right) left( 1 + {{%isigma'_y} over {j %iomega %ivarepsilon_0}} right) left( 1 + {{%isigma'_z} over {j %iomega %ivarepsilon_0}} right)^-1 H_z(%iomega) = -{ c_0 over %imu_zz } left[ {partial tilde E_y(%iomega)} over {partial x} - {partial tilde E_x(%iomega)} over {partial y} right]	(L13.S59a)

j %iomega left( 1 + {{%isigma'_x} over {j %iomega %ivarepsilon_0}} right)^-1 left( 1 + {{%isigma'_y} over {j %iomega %ivarepsilon_0}} right) left( 1 + {{%isigma'_z} over {j %iomega %ivarepsilon_0}} right) tilde D_x(%iomega) = c_0 left[ {partial H_z(%iomega)} over {partial y} - {partial H_y(%iomega)} over {partial z} right] - { %isigma_xx over %ivarepsilon_0 } tilde E_x(%iomega) newline j %iomega left( 1 + {{%isigma'_x} over {j %iomega %ivarepsilon_0}} right) left( 1 + {{%isigma'_y} over {j %iomega %ivarepsilon_0}} right)^-1 left( 1 + {{%isigma'_z} over {j %iomega %ivarepsilon_0}} right) tilde D_y(%iomega) = c_0 left[ {partial H_x(%iomega)} over {partial z} - {partial H_z(%iomega)} over {partial x} right] - { %isigma_yy over %ivarepsilon_0 } tilde E_y(%iomega) newline j %iomega left( 1 + {{%isigma'_x} over {j %iomega %ivarepsilon_0}} right) left( 1 + {{%isigma'_y} over {j %iomega %ivarepsilon_0}} right) left( 1 + {{%isigma'_z} over {j %iomega %ivarepsilon_0}} right)^-1 tilde D_z(%iomega) = c_0 left[ {partial H_y(%iomega)} over {partial x} - {partial H_x(%iomega)} over {partial y} right] - { %isigma_zz over %ivarepsilon_0 } tilde E_z(%iomega)	(L13.S59b)

Assume no real loss (σ) in the PML areas.

Convert to time domain using:
F lbrace d^a over dt^a g(t) rbrace = (j %iomega)^a G(%iomega)	(L14.S11)

To transform first equation in (13.59a), pull out Curl terms:
C_x^E(%iomega) ~=~ {partial tilde E_z(%iomega)} over {partial y} - {partial tilde E_y(%iomega)} over {partial z}	(L14.S12b)

Leaving:
j %iomega left( 1 + {{%isigma'_x} over {j %iomega %ivarepsilon_0}} right)^-1 left( 1 + {{%isigma'_y} over {j %iomega %ivarepsilon_0}} right) left( 1 + {{%isigma'_z} over {j %iomega %ivarepsilon_0}} right) H_x(%iomega) ~=~ -{ c_0 over %imu_xx } C_x^E(%iomega)	(L14.S12c)

Move first (inverted) parenthesized term to right side and multiply everything out:
j %iomega H_x(%iomega) + {%isigma'_y + %isigma'_z} over %ivarepsilon_0 H_x(%iomega) + 1 over {j %iomega} { {%isigma'_y %isigma'_z} over %ivarepsilon_0^2 } H_x(%iomega) ~=~ -{ c_0 over %imu_xx } C_x^E(%iomega) - 1 over {j %iomega} { {c_0 %isigma'_x} over {%ivarepsilon_0 %imu_xx} } C_x^E(%iomega)	(L14.S13c)

Apply (14.11) to get time-domain equation with PML:

{partial H_x(t)} over {partial t} + {%isigma'_y + %isigma'_z} over %ivarepsilon_0 H_x(t) + int from {- %infinite } to {t} { {%isigma'_y %isigma'_z} over %ivarepsilon_0^2 } H_x(%itau) d %itau ~ = ~ -{ c_0 over %imu_xx } C_x^E(t) - int from {- %infinite } to {t} { {c_0 %isigma'_x} over {%ivarepsilon_0 %imu_xx} } C_x^E(%itau) d %itau	(L14.S15)

Pull constant terms out of integrals:
{partial} over {partial t} H_x(t) ~+~ {%isigma'_y + %isigma'_z} over %ivarepsilon_0 H_x(t) ~+~ { {%isigma'_y %isigma'_z} over %ivarepsilon_0^2 } int from {- %infinite } to {t} H_x(%itau) d %itau ~=~ -{c_0 over %imu_xx} C_x^E(t) ~-~ { {c_0 %isigma'_x} over {%ivarepsilon_0 %imu_xx} } int from {- %infinite } to {t} C_x^E(%itau) d %itau	(L14.S16a)
Term 1. “This is the time derivative of the H field. We define the mag fields to exist at the half time steps, so this finite difference exists at the integer time steps, which is compatible with the electric field quantities.”:
{partial} over {partial t} H_x(t) ~~approx~~ { { H_{x,t+nospace{%iDELTA t}/2}^{i,j,k} - H_{x,t-nospace{%iDELTA t}/2}^{i,j,k} } over nospace{%iDELTA t} }	(L14.S19)
Term 2. Need an H that exists at the integer time step. So we interpolate the half time steps:
{%isigma'_y + %isigma'_z} over %ivarepsilon_0 H_x(t) ~~approx~~ {%isigma'_y^{i,j,k} + %isigma'_z^{i,j,k}} over { %ivarepsilon_0 } { { H_{x,t+nospace{%iDELTA t}/2}^{i,j,k} - H_{x,t-nospace{%iDELTA t}/2}^{i,j,k} } over 2 }	(L14.S20)
Term 3. Need to integrate up to time t, not t plus half. Pull out the last term in the summation:
int from {- %infinite } to {t} { {%isigma'_y %isigma'_z} over %ivarepsilon_0^2 } H_x(%itau) d %itau ~~approx~~ {%isigma'_y + %isigma'_z} over %ivarepsilon_0 sum from { T={nospace{%iDELTA t} / 2} } to {t+nospace{%iDELTA t} / 2} { H_{x,T}^{i,j,k} } nospace{%iDELTA t} newline ~~approx~~ {%isigma'_y + %isigma'_z} over %ivarepsilon_0 left ( color red {{ H_{x,t+nospace{%iDELTA t} / 2}^{i,j,k} } nospace{%iDELTA t} over 2} ~+~ sum from { T={nospace{%iDELTA t} / 2} } to color red {t-nospace{%iDELTA t} / 2} { H_{x,T}^{i,j,k} } nospace{%iDELTA t} right )	(L14.S22a)
Force the extracted term to only integrate over half of a time step:
int from {- %infinite } to {t} { {%isigma'_y %isigma'_z} over %ivarepsilon_0^2 } H_x(%itau) d %itau ~~approx~~ {%isigma'_y + %isigma'_z} over %ivarepsilon_0 left ( color green {( { H_{x,t+nospace{%iDELTA t} / 2}^{i,j,k} } + { H_{x,t-nospace{%iDELTA t} / 2}^{i,j,k} }) over 2 nospace{%iDELTA t} over 2} ~+~ sum from { T={nospace{%iDELTA t} / 2} } to {t-nospace{%iDELTA t} / 2} { H_{x,T}^{i,j,k} } nospace{%iDELTA t} right )	(L14.S22b)
Term 4. Just a curl operation:
-{c_0 over %imu_xx} C_x^E(t) ~~approx~~ -{c_0 over %imu_xx^{i,j,k}} C_{x,t}^{E,i,j,k}	(L14.S24a)
C_{x,t}^{E,i,j,k} ~=~ { { {tilde E}_{z,t}^{i,j+1,k} - {tilde E}_{z,t}^{i,j,k} } over nospace{%iDELTA y} } ~-~ { { {tilde E}_{y,t}^{i,j,k+1} - {tilde E}_{y,t}^{i,j,k} } over nospace{%iDELTA z} }	(L14.S24b)
Term 5. Integrating a term that exists at integer time steps.
-{ {c_0 %isigma'_x} over {%ivarepsilon_0 %imu_xx} } int from {- %infinite } to {t} C_x^E(%itau) d %itau ~~approx~~ {c_0 %isigma'_x^{i,j,k}} over {%ivarepsilon_0 %imu_xx^{i,j,k}} sum from { T=0 } to t { C_{x,T}^{E,i,j,k} } nospace{%iDELTA t}	(L14.S25)
Since the sum goes up to t instead of t+t/2, we'll be updating the sum before updating the E field.

Same procedure is used to derive the y and z equations.

To derive the update equation, substitute the terms and solve for the future time value of Hx, giving:
H_{x,t+nospace{%iDELTA t} / 2}^{i,j,k} ~=~ left( m_Hx1^{i,j,k} right) H_{x,t-nospace{%iDELTA t} / 2}^{i,j,k} ~+~ left( m_Hx2^{i,j,k} right) C_{x,t}^{E,i,j,k} ~+~ left( m_Hx3^{i,j,k} right) I_{CEx,t}^{i,j,k} ~+~ left( m_Hx4^{i,j,k} right) I_{Hx,t}^{i,j,k}	(L14.S33c)
with PML update coefficients:
alignl stack { alignc m_{Hx0}^{i,j,k} = 1 over nospace{%iDELTA t} + left( {%isigma_y^{H,i,j,k} + %isigma_z^{H,i,j,k}} over { 2 %ivarepsilon_0 } right) + {left( %isigma_y^{H,i,j,k} right) left( %isigma_z^{H,i,j,k} right) nospace{%iDELTA t}} over {4 %ivarepsilon_0^2} # alignc m_{Hx1}^{i,j,k} = 1 over m_{Hx0}^{i,j,k} left[ 1 over nospace{%iDELTA t} - left( {%isigma_y^{H,i,j,k} + %isigma_z^{H,i,j,k}} over { 2 %ivarepsilon_0 } right) - {left( %isigma_y^{H,i,j,k} right) left( %isigma_z^{H,i,j,k} right) nospace{%iDELTA t}} over {4 %ivarepsilon_0^2} right] # m_{Hx2}^{i,j,k} = {alignc -{1 over m_{Hx0}^{i,j,k}} { c_0 over %imu_x^{i,j,k}}} # m_{Hx3}^{i,j,k} = {alignc -{ 1 over m_{Hx0}^{i,j,k}} { nospace{c_0 %iDELTA t} over %ivarepsilon_0} { %isigma_x^{H,i,j,k} over %imu_xx^{i,j,k}}} # m_{Hx4}^{i,j,k} = {alignc -{1 over m_{Hx0}^{i,j,k}} { nospace{%iDELTA t} over %ivarepsilon_0^2} left( %isigma_y^{H,i,j,k} right) left( %isigma_z^{H,i,j,k} right)} }	(L14.S33a)
and integration terms:
I_{CEx,t}^{ i,j,k} ~=~ sum from { T=0 } to t { C_{x,T}^{E,i,j,k} } ~~~ I_{Hx,t-nospace{%iDELTA t} over 2}^{i,j,k} ~=~ sum from { T=0 } to {t-nospace{%iDELTA t} over 2} { H_{x,T}^{i,j,k} } newline newline C_{x,t}^{E,i,j,k} ~=~ { { {tilde E}_{z,t}^{i,j+1,k} - {tilde E}_{z,t}^{i,j,k} } over nospace{%iDELTA y} } ~-~ { { {tilde E}_{y,t}^{i,j,k+1} - {tilde E}_{y,t}^{i,j,k} } over nospace{%iDELTA z} }	(L14.S33b)
Similarly, the update equation for Dx is:
{tilde D}_{x,t+nospace{%iDELTA t}}^{i,j,k} ~=~ left( m_Dx1^{i,j,k} right) {tilde D}_{x,t}^{i,j,k} ~+~ left( m_Dx2^{i,j,k} right) C_{x,t+nospace{%iDELTA t} over 2}^{H,i,j,k} ~+~ left( m_Dx3^{i,j,k} right) I_{CHx,t-nospace{%iDELTA t} over 2}^{i,j,k} ~+~ left( m_Dx4^{i,j,k} right) I_{Dx,t-nospace{%iDELTA t}}^{i,j,k}	(L14.S39c)
with update coefficients:
alignl stack { alignc m_{Dx0}^{i,j,k} = 1 over nospace{%iDELTA t} + left( {%isigma_y^{D,i,j,k} + %isigma_z^{D,i,j,k}} over { 2 %ivarepsilon_0 } right) + {left( %isigma_y^{D,i,j,k} right) left( %isigma_z^{D,i,j,k} right) nospace{%iDELTA t}} over {4 %ivarepsilon_0^2} # alignc m_{Dx1}^{i,j,k} = 1 over m_{Dx0}^{i,j,k} left[ 1 over nospace{%iDELTA t} - left( {%isigma_y^{D,i,j,k} + %isigma_z^{D,i,j,k}} over { 2 %ivarepsilon_0 } right) - {left( %isigma_y^{D,i,j,k} right) left( %isigma_z^{D,i,j,k} right) nospace{%iDELTA t}} over {4 %ivarepsilon_0^2} right] # m_{Dx2}^{i,j,k} = {alignc {c_0 over m_{Dx0}^{i,j,k}}} # m_{Dx3}^{i,j,k} = {alignc { 1 over m_{Dx0}^{i,j,k}} {c_0 `nospace{%iDELTA t}` %isigma_x^{D,i,j,k}} over {%ivarepsilon_0}} # m_{Dx4}^{i,j,k} = {alignc -{1 over m_{Dx0}^{i,j,k}} { nospace{%iDELTA t} over %ivarepsilon_0^2} left( %isigma_y^{D,i,j,k} right) left( %isigma_z^{D,i,j,k} right)} }	(L14.S39a)

And integration terms:
stack{ I_{CHx,t-nospace{%iDELTA t} over 2}^{ i,j,k} ~=~ sum from { T=0 } to t-nospace{%iDELTA t} over 2 { C_{x,T}^{H,i,j,k} } ~~~ I_{Dx,t-nospace{%iDELTA t}}^{i,j,k} ~=~ sum from { T=0 } to {t-nospace{%iDELTA t}} { {tilde D}_{x,T}^{i,j,k} } # C_{x,t-nospace{%iDELTA t} over 2}^{H,i,j,k} ~=~ { { H_{z,t+nospace{%iDELTA t} over 2}^{i,j,k} - H_{z,t+nospace{%iDELTA t} over 2}^{i,j-1,k} } over nospace{%iDELTA y} } ~-~ { { H_{y,t+nospace{%iDELTA t} over 2}^{i,j,k} - H_{y,t+nospace{%iDELTA t} over 2}^{i,j,k-1} } over nospace{%iDELTA z} } }	(L14.S39b)
Update coefficients for Ex, Ey, Ez (εxx, etc. are εr):
m_{Ex1}^{i,j,k} = 1 over {{%ivarepsilon_xx}^{i,j,k}} ~~~ m_{Ey1}^{i,j,k} = 1 over {{%ivarepsilon_yy}^{i,j,k}} ~~~ m_{Ez1}^{i,j,k} = 1 over {{%ivarepsilon_zz}^{i,j,k}}	(L14.S42a)

Update equations:
{tilde E}_{x,t+nospace{%iDELTA t}}^{i,j,k} ~=~ left( m_Ex1^{i,j,k} right) {tilde D}_{x,t+nospace{%iDELTA t}}^{i,j,k} newline newline {tilde E}_{y,t+nospace{%iDELTA t}}^{i,j,k} ~=~ left( m_Ey1^{i,j,k} right) {tilde D}_{y,t+nospace{%iDELTA t}}^{i,j,k} newline newline {tilde E}_{z,t+nospace{%iDELTA t}}^{i,j,k} ~=~ left( m_Ez1^{i,j,k} right) {tilde D}_{z,t+nospace{%iDELTA t}}^{i,j,k}	(L14.S42b)
## My Transformations
size 10.5 {nospace {"Hatted variables ("hat %isigma") are my versions."}} From (13.46):
%isigma' = 2 %ivarepsilon_0 {hat %isigma} ~~~ L_i = n_b ~~~ b = n_b+1 ~~~ {hat %isigma}^H(i) = {1 over {2 %ivarepsilon_0}} %ivarepsilon_0 over {2 %iDELTA t} left( i over L_i right)^3 = 1 over {4 %iDELTA t} left( i over n_b right)^3

{hat %isigma}_x^{H,i,j,k} = left lbrace matrix { {hat %isigma}^H (b-i+1) # alignl for i<b ## 0 # alignl for b<=i<n_x-b ## {hat %isigma}^H (i-n_x+b) # alignl for i>=n_x-b} right none	(5.1)
    // pre-calc PML gradients (sH are shifted over 0.5)
    double* sHg = new double[nb];
    double* sEg = new double[nb];
    for (int i = 0; i < nb; i++) {
        double r = double(i) / nb;
        sEg[i] = r*r*r / (4*dt);
        r += 0.5 / nb;
        sHg[i] = r*r*r / (4*dt);
    }
       double sHx1 = (i < b) ? sHg[b-i-1] : ((i >= nx-b) ? sHg[i-nx+b] : 0.);
Common terms from (L14.S33a):
m_{Hx0}^{i,j,k} = 1 over {%iDELTA t} + A + B	(5.2)

A = {%isigma_y^{H,i,j,k} + %isigma_z^{H,i,j,k}} over { 2 %ivarepsilon_0 } = {{2 %ivarepsilon_0} left({hat %isigma}_y^{H,i,j,k} + {hat %isigma}_z^{H,i,j,k} right)} over { 2 %ivarepsilon_0 } = {{hat %isigma}_y^{H,i,j,k} + {hat %isigma}_z^{H,i,j,k}} newline newline B = {left( %isigma_y^{H,i,j,k} right) left( %isigma_z^{H,i,j,k} right) {%iDELTA t}} over {4 %ivarepsilon_0^2} = {left( {2 %ivarepsilon_0} {hat %isigma}_y^{H,i,j,k} right) left( {2 %ivarepsilon_0} {hat %isigma}_z^{H,i,j,k} right) {%iDELTA t}} over {4 %ivarepsilon_0^2} = {left( {hat %isigma}_y^{H,i,j,k} right) left( {hat %isigma}_z^{H,i,j,k} right) {%iDELTA t}}	(5.3)
// H update coefficients, mH2 & mH3 include "/dx"
double A = sHy + sHz;
double B = sHy * sHz * dt;
double R = 1 / (1/dt + A + B);
bp->mH1.x = R * (1/dt - A - B);
bp->mH2.x = -R * c0 / (dx * c.mur);
bp->mH3.x = -R * c0 * dt * sHx / (2 * dx);
bp->mH4.x = -R * 4*B;

Similar case for E common terms from (L14.S39a):

// E update coefficients (= D with 1/ep on H terms, 2 & 3)
A = sEy + sEz;
B = sEy * sEz * dt;
R = 1 / (1/dt + A + B);
bp->mE1.x = R * (1/dt - A - B);
bp->mE2.x = R * c0 / (dx * c.epr);
bp->mE3.x = R * c0 * dt * sEx / (2 * dx);
bp->mE4.x = -R * 4*B;
## Dimensional Analysis
Using [kg,m,s,A] exponents.
Henry = [1,2,-2,-2], Farad = [-1,-2,4,2], Volt = [1,2,-3,-1]
Norm Mag Field = sqrt(H/F)*A/m = ([1,2,-2,-2]-[-1,-2,4,2])/2+[0,-1,0,1]
 = [1,1,-3,-1] = V/m = Elec Field

Maxwell's equations
nabla times E = -%imu dH over dt ~~toward~~ (kg^1 m^0 s^-3 A^-1) = (kg^1 m^1 s^-2 A^-2)(kg^0 m^-1 s^-1 A^1) newline c_0^2 = 1 over { %imu_0 %ivarepsilon_0 } ~~toward~~ (kg^0 m^2 s^-2 A^0) = 1 over {(kg^1 m^1 s^-2 A^-2)(kg^-1 m^-3 s^4 A^2)} ✔	(5.4)

{ m_{Hx0}^{i,j,k} = 1 over {%iDELTA t} + left( {%isigma_y^{H,i,j,k} + %isigma_z^{H,i,j,k}} over { 2 %ivarepsilon_0 } right) + {left( %isigma_y^{H,i,j,k} right) left( %isigma_z^{H,i,j,k} right) {%iDELTA t}} over {4 %ivarepsilon_0^2} } ~~toward~~ {1 over (s^1) + {(s^-1 %ivarepsilon_0) over (%ivarepsilon_0)} + {{(s^-1 %ivarepsilon_0)(s^-1 %ivarepsilon_0)(s)} over (%ivarepsilon_0)^2}} ✔	(5.5)

{ m_{Hx1}^{i,j,k} = 1 over m_{Hx0}^{i,j,k} left[ {%isigma_y^{H,i,j,k} + %isigma_z^{H,i,j,k}} over { 2 %ivarepsilon_0 } - {left( %isigma_y^{H,i,j,k} right) left( %isigma_z^{H,i,j,k} right) {%iDELTA t}} over {4 %ivarepsilon_0^2} right] } ~~toward~~ {{1 over (s^-1)} {(s^-1)}} ~~toward~~ {1} ✔	(5.6)

{ {hat m}_{Hx2}^{i,j,k} = {alignc -{1 over m_{Hx0}^{i,j,k} { c_0 over {%imu_r^{i,j,k}nospace{%iDELTA x}}}}} } ~~toward~~ {1 over (s^-1)} {(m/s) over m} ~~toward~~ 1 ✔	(5.7)

{ {hat m}_{Hx3}^{i,j,k} = {alignc -{ 1 over m_{Hx0}^{i,j,k}} { {c_0 %iDELTA t} over %ivarepsilon_0} { %isigma_x^{H,i,j,k} over {%imu_r^{i,j,k} nospace{%iDELTA x}}}} } ~~toward~~ { 1 over (s^-1) { (kg^0 m^1 s^-1 A^0) (s) } over (%ivarepsilon_0) (s^-1 %ivarepsilon_0) over (m)} ~~toward~~ 1 ✔	(5.8)

{ m_{Hx4}^{i,j,k} = {alignc -{1 over m_{Hx0}^{i,j,k}} { {%iDELTA t} over %ivarepsilon_0^2} left( %isigma_y^{H,i,j,k} right) left( %isigma_z^{H,i,j,k} right)} } ~~toward~~ {1 over (s^-1) (s) over (%ivarepsilon_0)^2 (s^-1 %ivarepsilon_0)^2} ~~toward~~ 1 ✔	(5.9)

From http://personalpages.manchester.ac.uk/staff/fumie.costen/tmp/sourceexcitationpaperEMCblackwhite.pdf Eq (4):
nospace{%iDELTA E_z} = -nospace{%iDELTA t} over %ivarepsilon left [ I_z over {nospace{%iDELTA x} nospace{%iDELTA y}} right ] ~~toward~~ (kg^1 m^1 s^-3 A^-1) = {(s)(A)} over {(kg^-1 m^-3 s^4 A^2)(m)(m)} ✔	(5.10)
# Space::allocate() — Update Coefficients
Conduction form of Ez update equation, from Schneider:
color blue {E_z^{q+1}[m] ~=~ {{ 1-{%isigma %DELTA t} over {2 %iepsilon} } } over { 1+{%isigma %DELTA t} over {2 %iepsilon} } E_z^{q}[m] ~+~ {{ {%DELTA t} over {%iepsilon %DELTA x} } } over { 1+{%isigma %DELTA t} over {2%iepsilon} } left ( H_y^{q+1over2} left[ m+1over2 right] - H_y^{q+1over2} left[ m-1over2 right] right )}	(U3.52)
(These are expanded to 3 dimensions in ch. 9, (U9.15) - (U9.32))

In our notation, with coefficients separated:
E_{z,t+%DELTA t}^{i,j,k} ~=~ m_Ez1^{i,j,k} E_{z,t}^{i,j,k} ~+~ m_Ez2^{i,j,k} left ( H_{y,t+%DELTA t over 2}^{i,j,k} - H_{y,t+%DELTA t over 2}^{i,j-1,k} right ) newline m_Ez0^{i,j,k} = 1+{%isigma^E %DELTA t} over {2%ivarepsilon},~~ m_Ez1^{i,j,k} = {1 over m_Ez1^{i,j,k}} left[ 1-{%isigma^E %DELTA t} over {2 %ivarepsilon} right],~~ m_Ez2^{i,j,k} = {1 over m_Ez1^{i,j,k}} left[ { {%DELTA t} over {%ivarepsilon %DELTA x} } right],	(6.1)
Compare with PML coefficients:
m_{Ex0}^{i,j,k} = 1 over nospace{%iDELTA t} + left( {%isigma_y^{D,i,j,k} + %isigma_z^{D,i,j,k}} over { 2 %ivarepsilon_0 } right) + {left( %isigma_y^{D,i,j,k} right) left( %isigma_z^{D,i,j,k} right) nospace{%iDELTA t}} over {4 %ivarepsilon_0^2} newline m_{Ex1}^{i,j,k} = 1 over m_{Ex0}^{i,j,k} left[ 1 over nospace{%iDELTA t} - left( {%isigma_y^{D,i,j,k} + %isigma_z^{D,i,j,k}} over { 2 %ivarepsilon_0 } right) - {left( %isigma_y^{D,i,j,k} right) left( %isigma_z^{D,i,j,k} right) nospace{%iDELTA t}} over {4 %ivarepsilon_0^2} right] newline {hat m}_{Ex2}^{i,j,k} = left( 1 over %ivarepsilon_r right) {c_0 over {m_{Ex0}^{i,j,k} nospace {%iDELTA x}}}	(14.39a, 14.42)
If sigmas are isotropic:
m_{Ex0}^{i,j,k} = 1 over nospace{%iDELTA t} + left( {%isigma^{D,i,j,k}} over { %ivarepsilon_0 } right) + {left( %isigma^{D,i,j,k} right)^2 nospace{%iDELTA t}} over {4 %ivarepsilon_0^2} newline m_{Ex1}^{i,j,k} = 1 over m_{Ex0}^{i,j,k} left[ 1 over nospace{%iDELTA t} - left( {%isigma^{D,i,j,k}} over { %ivarepsilon_0 } right) - {left( %isigma^{D,i,j,k} right)^2 nospace{%iDELTA t}} over {4 %ivarepsilon_0^2} right] newline {hat m}_{Ex2}^{i,j,k} = c_0 over {%ivarepsilon_r m_{Ex0}^{i,j,k} nospace{%iDELTA x}}	(6.2)
Or:
{m_{Ex1}^{i,j,k} = { 1 - B } over { 1 + B }}, ~~ {B = 2A + A^2}, ~~ A = {%isigma^{E,i,j,k} nospace{%iDELTA t}} over {2 %ivarepsilon_0} newline {hat m}_{Ex2}^{i,j,k} = {c_0 nospace{%iDELTA t}} over {%ivarepsilon_r nospace{%iDELTA x} (1 + B)}	(6.3)
So it appears to be equivalent, other than the PML version is a 2nd order approximation.
## Dimensional Analysis
Dimensional analysis follows that for the PML in section 5.2. For sigma E specifically:

{%isigma^E nospace{%iDELTA t}} over {%ivarepsilon_0} = k ~toward~ {(kg^-1 m^-3 s^3 A^2) (s)} over (kg^-1 m^-3 s^4 A^2) = 1 ✔	(6.4)
color blue { left( 1+{%isigma %DELTA t} over {2 %iepsilon} right)E_z^{q+1}[m] ~=~ {left( 1-{%isigma %DELTA t} over {2 %iepsilon} right) } E_z^{q}[m] ~+~ {{ {%DELTA t} over {%iepsilon %DELTA x} } } left ( H_y^{q+1over2} left[ m+1over2 right] - H_y^{q+1over2} left[ m-1over2 right] right )}	(6.5)
# Space::stepH(), E() — Update Equations
## Derivation of My Update Coefficients

%imu {left none {partial H_y} over {partial t} right rline}_{ (m+1/2) %iDELTA x, q %iDELTA t }

These are from Schneider

del(E) = -mu*d(H)/dt
c0^2 = 1/(mu0*ep0)

Normalizing mag field: (here Hu is unnormalized H)
Using H = sqrt(mu0/ep0)*Hu
 So: del(E) = -mu*d(Hu)
     del(E) = -mu*(1/sqrt(mu0/ep0))*d(H)
     del(E) = -mu*(sqrt(mu0/ep0)/(mu0/ep0))*d(H)
     del(E) = -mur*(sqrt(mu0/ep0)*ep0)*d(H)
     del(E) = -mur*((sqrt(mu0)*ep0)/sqrt(ep0))*d(H)
     del(E) = -mur*((sqrt(mu0)*ep0*sqrt(ep0))/ep0)*d(H)
     del(E) = -mur*(1/c0))*d(H)
     del(E) = -(mur/c0)*d(H)

Without conduction (sigma):
Kmu = dt*c0/(mur*dx) = 1 when dt/dx = c0
mu = mu0 * mur
c0^2 = (mur*epr)/(mu*ep)

With conduction:
stm = sig*dt/(2*mu)
Hx = (1-stm)/(1+stm)*Hx + (dt/((1+stm)*mu*dx))*(Eyp1-Ey)-(Ezp1-Ez))

From [Sch2018] 3.12 Lossy Material. Ampere's law with conduction term:
del(Hu) = sig*E + ep*d(E) [eq 3.48]
color blue {%isigma vec E + %ivarepsilon { partial vec E } over { partial t } = nabla times vec H }	(U3.48)
In discretized form:
dHu/dx = sig*E + ep*dE/dt
color blue {%isigma E_x + %ivarepsilon {partial E_x} over {partial t} = {partial H_y} over {partial x}}	(U3.49)
1D version, averaging in time the E node on either side of the H node:
(Huyp1 - Huy)/dx = sig*(Ezp1 + Ez)/2 + ep*(Ezp1 - Ez)/dt
{ H_{y,t+{%iDELTA t} over 2}^{i,j,k+1} - H_{y,t-{%iDELTA t} over 2}^{i,j,k} } over {%iDELTA x} = %isigma left( E_{z,t}^{i,j+1,k} - E_{z,t}^{i,j,k} right) over 2 + %ivarepsilon left( E_{z,t}^{i,j+1,k} - E_{z,t}^{i,j,k} right) over {%iDELTA t}	(U3.51?)

Ezp1 = ((Huyp1 - Huy)/dx - (sig/2 - ep/dt)*Ez) / (sig/2 + ep/dt)

Ezp1 = (1/(dx*(sig/2 + ep/dt)))*(Hyup1 - Huy) -
        ((sig/2 - ep/dt)/(sig/2 + ep/dt))*Ez

Ezp1 = (dt/(dx*ep*(sig*dt/(2*ep) + 1))*(Huyp1 - Huy) -
        ((sig*dt/(2*ep) - 1)/(sig*dt/(2*ep) + 1))*Ez

Ezp1 = ((dt/(dx*ep))/(1 + sig*dt/(2*ep))*(Huyp1 - Huy) +
        ((1 - sig*dt/(2*ep))/(1 + sig*dt/(2*ep)))*Ez
color blue {E_z^{q+1}[m] ~=~ {{ 1-{%isigma %DELTA t} over {2 %iepsilon} } } over { 1+{%isigma %DELTA t} over {2 %iepsilon} } E_z^{q}[m] ~+~ {{ {%DELTA t} over {%iepsilon %DELTA x} } } over { 1+{%isigma %DELTA t} over {2%iepsilon} } left ( H_y^{q+1over2} left[ m+1over2 right] - H_y^{q+1over2} left[ m-1over2 right] right )}	(U3.52)

Ezp1 = ((dt/(dx*ep))/(1 + sig*dt/(2*ep))*(Hyp1 - Hy)/Z0 +
        ((1 - sig*dt/(2*ep))/(1 + sig*dt/(2*ep)))*Ez

Z0 = 1/(ep0*c0)
%ieta_0 = sqrt{%imu_0 over %ivarepsilon_0} newline c_0 = 1 over sqrt{%imu_0 %ivarepsilon_0} ~~~ %ieta_0 = 1 over {%ivarepsilon_0 c_0} = %imu_0 c_0
non Kep = dt*c0/(dx*ep0*epr)
m_2^E = {%iDELTA t ` c_0} over {%iDELTA x ` %ivarepsilon_0 %ivarepsilon_r}	?

sig Kep = dt/(Z0*dx*ep0*epr) = dt*(ep0*c0)/(dx*ep0*epr)

Huyp1 = ((dt/(dx*mu))/(1 + sig*dt/(2*mu))*(Ezp1 - Ez) +
        ((1 - sig*dt/(2*mu))/(1 + sig*dt/(2*mu)))*Huy

Hyp1/Z0 = ((dt/(dx*mu))/(1 + sig*dt/(2*mu))*(Ezp1 - Ez) +
        ((1 - sig*dt/(2*mu))/(1 + sig*dt/(2*mu)))*Hy/Z0

Hyp1 = ((dt/(dx*mu))/(1 + sig*dt/(2*mu))*(Ezp1 - Ez)*Z0 +
        ((1 - sig*dt/(2*mu))/(1 + sig*dt/(2*mu)))*Hy

non Kmu = dt*c0/(dx*mu0*mur)
m_2^H = {%iDELTA t ` c_0} over {%iDELTA x ` %imu_0 %imu_r}	?

sig Kmu = dt*Z0/(dx*mu0*mur) = dt/(dx*ep0*c0*mu0*mur)
  = dt*c0/(dx*ep0*c0^2*mu0*mur) = dt*c0/(dx*mur)

ste = sig*dt/(2*ep) = sig*dt/(2*ep0*epr)
Ksep = (1 - ste) / (1 + ste)
Kep = (dt/(dx*ep0*epr)) / (1 + ste)
# OuterSpace::stepH(), E() — Conduction Border
?
Originally had (field_main2_844.cp, 180216):

        if (copyBorders)
        {
        // update E field borders
        for (size_t i = 1; i < nx-1; i++)
        for (size_t j = 1; j < ny-1; j++)
        {
        Et(i,j,0) = Et(i,j,1);
        Et(i,j,nz-1) = Et(i,j,nz-2);
        }
        for (size_t i = 1; i < nx-1; i++)
        for (size_t k = 1; k < nz-1; k++)
        {
        Et(i,0,k) = Et(i,1,k);
        Et(i,ny-1,k) = Et(i,ny-2,k);
        }
        for (size_t j = 1; j < ny-1; j++)
        for (size_t k = 1; k < nz-1; k++)
        {
        Et(0,j,k) = Et(1,j,k);
        Et(nx-1,j,k) = Et(nx-2,j,k);
        }
        }

Then (field_main2.cp@6777, 180216):
r6777 | scott | 2018-02-16 13:13:27 -0700 (Fri, 16 Feb 2018) | 2 lines
Changed copyBorders option to conductBorder, which matches small_lc_wall.out quite closely.

        // conductive border: tangential E and normal H are zero
        if (conductBorder)
        {
        for (size_t i = 1; i < nx-1; i++)
        {
        double3* Hp = &Ht(i,1,0);
        double3* Ep = &Et(i,1,0);
        double* Kmup = &Kmut(i,1,0);
        for (size_t j = 1; j < ny-1; j++)
        {
        // step all H[i,j,0], but with z terms removed
        double Km = *Kmup;
        Hp->x += Km * ((Ep+1)->y - Ep->y);
        Hp->y -= Km * ((Ep+1)->x - Ep->x);
        // want H[i,j,nz-1], but it reaches beyond border
        //double3* En = Ep + (nz-1)*k1;
        //double3* Hn = Hp + (nz-1)*k1;
        //Hn->x += Km * ((En+k1)->y - En->y);
        //Hn->y -= Km * ((En+k1)->x - En->x);
        Kmup += J1;
        Ep += J1;
        Ep += J1;
        }
        }

# Notes
180311:

Normalizing H:
nabla times vec E = -[%imu] {partial vec H} over {partial t} ~~~ nabla times vec H = [%ivarepsilon] {partial vec E} over {partial t} newline {vec tilde H = sqrt {%imu_0 over %ivarepsilon_0} vec H = %ieta_0 vec H} ~~toward~~ matrix { {nabla times vec E = -{[%imu_0 %imu_r] over %ieta_0} {partial vec tilde H} over {partial t}} ## {nabla times vec tilde H = %ieta_0 [%ivarepsilon_0 %ivarepsilon_r] {partial vec E} over {partial t}} } ~~toward~~ matrix { {nabla times vec E = -{[%imu_r] over c_0} {partial vec tilde H} over {partial t}} ## {nabla times vec tilde H = {[%ivarepsilon_r] over c_0} {partial vec E} over {partial t}} }	(L5.S21)
Normalizing E (same equations, just different scales to the physical values):
{vec tilde E = sqrt {%ivarepsilon_0 over %imu_0} vec E = vec E over %ieta_0} ~~toward~~ matrix { {nabla times vec tilde E = -{[%imu_0 %imu_r] over %ieta_0} {partial vec H} over {partial t}} ## {nabla times vec H = %ieta_0 [%ivarepsilon_0 %ivarepsilon_r] {partial vec tilde E} over {partial t}} } ~~toward~~ matrix { {nabla times vec tilde E = -{[%imu_r] over c_0} {partial vec H} over {partial t}} ## {nabla times vec H = {[%ivarepsilon_r] over c_0} {partial vec tilde E} over {partial t}} }	(9.1)
Rearranging for Update Equation form:
matrix { {vec H = -{c_0 over [%imu_r]} int {left( nabla times vec tilde E right) dt}} ## {vec tilde E = {c_0 over [%ivarepsilon_r]} int {left( nabla times vec H right) dt}} }	(9.2)
The existing non-PML coefficient calculations look correct, at least for the σ = 0 case (and they match LC).
How can the PML not match? It should just attenuate whatever levels of H & E it's given. Its coefficient values should match across the PML-center seam.

non-PML: mH2 = (dt/dx) * Z0 / (mu0*mur)
PML: mH2 = (dt/dx) * c0 / (mu0*mur) ???

There shouldn't be a mu0 (or ep0) in the PML case. See (13.58). muxx is relative, not absolute.

-----------------
180315:

alignl size 10.5 "“It is possible for the charge in materials to move under the influence of an electric field such that currents flow. If" newline alignl size 10.5 nospace{"the material has a non-zero conductivity "%isigma ", the current density is given by"}
vec J = %isigma vec E.	(U2.38)
“The current density has units of A/m2 and the conductivity has units of S/m.” [Sch2018]

 -----------------
180504:

Checking how the sigmas of Space::allocate() and initPMLarea() correlate.

1/c0 = sqrt(mu0) * sqrt(ep0);
z0 = sqrt(mu0) / sqrt(ep0);
z0 = (1/(sqrt(ep0)*c0)) / sqrt(ep0);
z0 = 1/(ep0*c0);
c0 = 1/(z0*ep0);

----------
allocate():
mE1.z[i] = (1. - (sige[i]*dt / (2*ep0*epr[i]))) / (1. + (sige[i]*dt / (2*ep0*epr[i])));

mE2.z[i] = (dt/dx) / ((1. + (sige[i]*dt / (2*ep0*epr[i]))) * z0*ep0*epr[i]);

----------
initPMLarea():
mE1.z[i] = (1 / (1/dt + (r*r*r / (4*dt)))) * (1/dt - (r*r*r / (4*dt)));

mE2.z[i] = (1 / (1/dt + (r*r*r / (4*dt)))) * c0 / (dx * epr[i]);
mE2.z[i] = (1 / ((1/dt)(1 + r*r*r/4))) * c0 / (dx * epr[i]);
mE2.z[i] = (dt / (1 + r*r*r/4)) * c0 / (dx * epr[i]);
mE2.z[i] = (dt / (1 + r*r*r/4)) / (dx * z0*ep0*epr[i]);
mE2.z[i] = (dt/dx) / (1 + r*r*r/4) / (z0*ep0*epr[i]);

SVN revision $Id: $